## Slide 1
Universality

## Slide 2
Universal SET
Is it possible to implement ALL the possible Boolean functions using NOT, AND, OR, NAND, NOR? Yes!

## Slide 3
Universal SET
What if we are not given some!
What if some are very costly! E.g., NOT
Can we reduce this set? E.g., building NOT by NAND/ NOR

## Slide 4
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = NOT-AND NOR = NOT-OR
{NOT, AND} | If we could design OR
{NOT, OR} | If we could design AND
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 5
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR (a Complete Set)
{NOT, OR} | If we could design AND (a Complete Set)
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 6
Universal SET
{NOT, AND}

## Slide 7
De Morgan's laws
► (Y+X)’= Y’X’
Augustus De Morgan
(1806–1871)
Mathematician
Logician

## Slide 8
X
Y
X’
Y’
Y’X’=(Y+X)’
Y+X

## Slide 9
X
Y
Y+X
OR

## Slide 10
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR (a Complete Set)
{NOT, OR} | If we could design AND (a Complete Set)
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 11
Universal SET
{NOT, OR}

## Slide 12
De Morgan's laws
► Y’+X’ = (YX)’
Augustus De Morgan
(1806–1871)
Mathematician
Logician

## Slide 13
X
Y
X’
Y’
Y’+X’=(YX)’
YX

## Slide 14
X
Y
YX
AND

## Slide 15
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR (a Complete Set)
{NOT, OR} | If we could design AND (a Complete Set)
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 16
Universal GATE
{NAND}

## Slide 17
NOT ► (XX)’ = (X↑X) = X’
X
X’

## Slide 18
AND►NOT (NAND) = ((Y↑X))’=YX
X
(Y↑X)
Y
(Y↑X)’= YX

## Slide 19
OR ► DE Morgan's law
(Y+X)’ = Y’X’
((Y+X)’)’ = (Y’X’)’
Y + X = (Y’X’)’
Y + X = Y’ ↑ X’

## Slide 20
OR: DE Morgan's law
X
X’
Y
Y’
(Y’X’)’ =
Y+X =
Y’ ↑ X’

## Slide 21
https://commons.wikimedia.org/wiki/7400_series_overview

## Slide 22
X
X
X’
Y
Y
Y’
Y’
X’
Y+X

## Slide 23
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR (a Complete Set)
{NOT, OR} | If we could design AND (a Complete Set)
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 24
Universal GATE
{NOR}

## Slide 25
NOT ► (X+X)’ = (XX) = X’
OR ► NOT (NOR)
AND ► De Morgan's law
(Y’+X’)’ = YX = (Y’↓X’)

## Slide 27
https://commons.wikimedia.org/wiki/7400_series_overview

## Slide 28
X
X
X’
Y
Y
Y’
Y’
X’
YX

## Slide 29
Design
a design algorithm for any digital units (logic circuits), given truth table

## Slide 30
minterm
aka. Standard Product

## Slide 31
X’ vs. x
1 binary variable appear either:
in its normal form X, or
in its complement form X’

## Slide 32
m0 | X’
m1 | X

## Slide 33
YX vs. YX’ vs. Y’x vs. Y’X’
2 binary variables appear either in one of these forms:

## Slide 34
m0 | Y’X’
m1 | Y’X
m2 | YX’
m3 | YX

## Slide 35
ZYX vs. ZYX’ vs. …
3 binary variables appear either in one of these forms: how many?

## Slide 36
ZYX vs. ZYX’ vs. …
3 binary variables appear either in one of these forms: how many?
Each variable can take 2 forms (normal and complement)
We have 3 variables, 2×2×2 = 23 = 8

## Slide 37
m0 | Z’Y’X’
m1 | Z’Y’X
m2 | Z’YX’
m3 | Z’YX
m4 | ZY’X’
m5 | ZY’X
m6 | ZYX’
m7 | ZYX

## Slide 38
An…A2A1A0 vs. An…A2A1A’0 …
n binary variables appear either in one of these forms: how many?
Each variable can take 2 forms (normal and complement)
We have n variables, 2×2×2× … ×2 = 2n

## Slide 39
m0 | A’n…A’2A’1A’0
m1 | A’n…A’2A’1A0
m2 | A’n…A’2A1A’0
… | …
… | …
m2n-3 | An…A2A’1A0
m2n-2 | An…A2A1A’0
m2n-1 | An…A2A1A0

## Slide 40
Truth table
en.wikipedia.org/wiki/Truth_table

## Slide 41
X | F = F(X) = ?
0 | ?
1 | ?

## Slide 42
X | F = F(X) = 1
0 | 1
1 | 1

## Slide 43
X | F = F(X) = 0
0 | 0
1 | 0

## Slide 44
X | F = F(X) = X’
0 | 1
1 | 0

## Slide 45
m0 | X’
m1 | X

## Slide 46
X | F = F(X) = X’ = m0
0 | 1
1 | 0

## Slide 47
X | F = F(X) = X’ = m0
0 | 1
1 | 0

## Slide 48
X
F = X’=m0

## Slide 49
X | F = F(X) = X
0 | 0
1 | 1

## Slide 50
X | F = F(X) = X = m1
0 | 0
1 | 1

## Slide 51
X | F = F(X) = X = m1
0 | 0
1 | 1

## Slide 52
X
F = X=m1
Digital Buffer
X
X’
X

## Slide 53
Truth table ↔ minterm

## Slide 54
Y | X | F = F(Y,X) = ?
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?

## Slide 55
Y | X | F = F(Y,X) = 0
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 56
Y | X | F = F(Y,X) = 1
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 57
Y | X | F = F(Y,X) = YX
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 58
X
F = YX
Y

## Slide 59
m0 | Y’X’
m1 | Y’X
m2 | YX’
m3 | YX

## Slide 60
Y | X | F = F(Y,X) = YX =m3
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 61
Y | X | F = F(Y,X) = YX =m3
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 62
Y | X | F = F(Y,X) = YX’ =m2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0

## Slide 63
Y | X | F = F(Y,X) = YX’ =m2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0

## Slide 64
X
F = YX’
Y

## Slide 65
Y | X | F = F(Y,X) = Y’X =m1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 66
Y | X | F = F(Y,X) = Y’X =m1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 67
X
F = Y’X
Y

## Slide 68
Y | X | F = F(Y,X) = Y’X’ =m0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 69
Y | X | F = F(Y,X) = Y’X’ =m0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 70
X
F = Y’X’
Y

## Slide 71
Y | X | F = F(Y,X) = ?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 72
Y | X | F = F(Y,X) = Y’X’
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 73
Y | X | F = F(Y,X) = Y’X’+Y’X
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 74
Y | X | F = F(Y,X) = m0+m1
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 75
Y | X | F = F(Y,X) = ∑m(0,1)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 76
X
Y
Y’X’
Y’X
Y’X’+Y’X

## Slide 77
X
Y
Y’X’
Y’X
Y’X’+Y’X

## Slide 78
Y | X | F = F(Y,X) = ?
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 79
Y | X | F = F(Y,X) = Y’X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 80
Y | X | F = F(Y,X) = m1+m2
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 81
Y | X | F = F(Y,X) = ∑m(1,2)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 82
X
Y
Y’X
YX’
Y’X+YX’
X
Y

## Slide 83
Y | X | F = F(Y,X) = Y’X+YX’ = m1+m2
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
X
Y
Y+X
Exclusive-OR (XOR)

## Slide 84
Y | X | F = F(Y,X) = ?
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 85
Y | X | F = F(Y,X) = Y’X’
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 86
Y | X | F = F(Y,X) = Y’X’+YX
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 87
Y | X | F = F(Y,X) = m0+m3
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 88
Y | X | F = F(Y,X) = ∑m(0,3)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 89
X
Y
Y’X’
YX
Y’X’+YX
X
Y

## Slide 90
Y | X | F = F(Y,X) = Y’X’+YX = m0+m3
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X
Y
Y X
NOT Exclusive-OR (XNOR)

## Slide 91
Y | X | F = F(Y,X) = ?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 92
Y | X | F = F(Y,X) = Y’X’
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 93
Y | X | F = F(Y,X) = Y’X’+Y’X
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 94
Y | X | F = F(Y,X) = Y’X’+Y’X+YX
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 95
Y | X | F=F(Y,X)=m0+m1+m3 =∑m(0,1,3)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 96
X
Y
Y’X’
Y’X
Y’X’+Y’X+YX
X
Y
YX

## Slide 97
SUM OF PRODUCTS
(SOP)

## Slide 98
X
Y
Y’X’
Y’X
Y’X’+Y’X+YX
X
Y
YX

## Slide 99
2 LEVELS
AND  OR

## Slide 100
X
Y
Y’X’
Y’X
Y’X’+Y’X+YX
X
Y
YX

## Slide 101
Given 3 inputs, design a circuit to determine if there is even number of 1

## Slide 102
Z | Y | X | F(Z,Y,X)=?
0 | 0 | 0 | ?
0 | 0 | 1 | ?
0 | 1 | 0 | ?
0 | 1 | 1 | ?
1 | 0 | 0 | ?
1 | 0 | 1 | ?
1 | 1 | 0 | ?
1 | 1 | 1 | ?

## Slide 103
Z | Y | X | F(Z,Y,X)=?
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 104
Z | Y | X | F(Z,Y,X)=Z’Y’X’
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 105
Z | Y | X | F(Z,Y,X)=Z’Y’X’+Z’YX
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 106
Z | Y | X | F(Z,Y,X)=Z’Y’X’+Z’YX+ZY’X
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 107
Z | Y | X | F(Z,Y,X)=Z’Y’X’+Z’YX+ZY’X+ZYX’
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 108
Z | Y | X | F(Z,Y,X)=m0+m3+m5+m6
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 109
Z | Y | X | F(Z,Y,X)=m0+m3+m5+m6=∑m(0,3,5,6)
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 110
X
Y
Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z

## Slide 111
SUM OF PRODUCTS (SOP)
2 LEVELS AND-OR

## Slide 112
X
Y
Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z

## Slide 113
X
Y
Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z