## Slide 1
Minimization
aka. Simplification

## Slide 2
Claude Elwood Shannon
Mathematician
Electrical Engineer
Cryptographer
M.Sc. Thesis (1937)
A Symbolic Analysis of Relay and Switching Circuits
Switching Algebra!
2-valued Boolean algebra
Notes: He is also well known for founding digital circuit design theory in 1937, when—as a 21-year-old master's degree student at the Massachusetts Institute of Technology (MIT)—he wrote his thesis demonstrating that electrical applications of Boolean algebra could construct any logical numerical relationship

## Slide 3
Switching algebra
Given S={0,1}
Given § = × (AND), † = + (OR)
S is closed, commutative, and distributive w.r.t × , +
e× = 1 and e+ = 0
Complement: for any x S, there is yS such that
  0 × 1 = e+ = 0
  0 + 1 = e× = 1
  We denote 0=1’, 1=0’

## Slide 4
Switching algebra
Is-A
Boolean algebra
It satisfies all conditions of Boolean algebra!
Prove  Book: 2.3 axiomatic definition of Boolean algebra

## Slide 5
Another sample of algebra in CS:
Relational Algebra (SQL)
Is relational algebra a Boolean algebra? Check this when you take
COMP-3150: Database Management Systems!

## Slide 6
Basic Theorems
Prove by postulates

## Slide 7
X + X = X
X+ X + X + … + X = X

## Slide 8
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1

## Slide 9
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1
= (X + X) (X+X’) using complement property

## Slide 10
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1
= (X + X) (X+X’) using complement property
= X + (XX’) using distributive property of + over ×

## Slide 11
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1
= (X + X) (X+X’) using complement property
= X + (XX’) using distributive property of + over ×
= X + 0 using complement property

## Slide 12
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1
= (X + X) (X+X’) using complement property
= X + (XX’) using distributive property of + over ×
= X + 0 using complement property
= X using identity property of e+=0

## Slide 13
X + 1 = 1
X+ Y + Z + … + 1 = 1

## Slide 14
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1

## Slide 15
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1
= (X + 1) (X+X’) using complement property

## Slide 16
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1
= (X + 1) (X+X’) using complement property
= X + (1X’) using distributive property of + over ×

## Slide 17
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1
= (X + 1) (X+X’) using complement property
= X + (1X’) using distributive property of + over ×
= X + X’ using identity e×=1

## Slide 18
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1
= (X + 1) (X+X’) using complement property
= X + (1X’) using distributive property of + over ×
= X + X’ using identity e×=1
= 1 using complement property

## Slide 19
X + xy = x
X + xY + xZW + … + xwAD = x
Absorption

## Slide 20
X + xy = x
X + xY + xZW + … + xwAD = x
X + xy =
= X1+XY using identity e×=1
= x(1 + Y) using distributive property of × over +
= X1 using previous theorem x+1=1
= X using identity e×=1
Absorption

## Slide 21
duality
    Dual(F) = OR AND, 1 0
    Dual(F) may or may not equal to F!

## Slide 22
duality
X+1 X0
X+X’ XX’
(X+Y)’ (XY)’

## Slide 23
duality
A postulate or a proved theorem for F
Also a postulate or a proved theorem for Dual(F)

## Slide 24
duality
{X+1=1} {X0 = 0}
{X+X’=1} {XX’=0}k
{(X+Y)’=X’Y’} {(XY)’=X’+Y’}

## Slide 25
X(x+y) = x
X(x+Y)(x+Z) … (x+w) = x
{X(x+y)= X} {X+XY=X}
We proved the dual version
Using the duality property, this is also true!
Absorption

## Slide 26
Basic Theorems
prove by truth table
For equality proof, F1=F2, for all possibility in the input variables (all rows), both side of equation must have equal value for same input variables.
For inequality proof, F1≠F2, find at least one possibility (a row) that have different values.

## Slide 27
Minimization
Boolean Algebra (algebraically)
aka. Algebraic Manipulation

## Slide 28
F = zy’x’+ zYX + Zyx’ + zy’X
4 × 3-input-and
1 × 4-input-OR

## Slide 29
F = zy’x’+ zYX + Zyx’ + zy’X

## Slide 30
F = z (y’x’ + yx + yx’ + y’x)

## Slide 31
F = z (y’x’ + yx + yx’ + y’x)

## Slide 32
F = z (y’(x’+X) + yx + yx’)

## Slide 33
F = z (y’(x’+X) + yx + yx’)

## Slide 34
F = z (y’ 1 + yx + yx’)

## Slide 35
F = z (y’ 1 + yx + yx’)

## Slide 36
F = z (y’ + yx + yx’)

## Slide 37
F = z (y’ + yx + yx’)

## Slide 38
F = z (y’ + y (x+X’))

## Slide 39
F = z (y’ + y (x+X’))

## Slide 40
F = z (y’ + y1)

## Slide 41
F = z (y’+y)

## Slide 42
F = z (y’+y)

## Slide 43
F = z1

## Slide 44
F = z
0 gates!

## Slide 45
F = zy’x’ + zyx+ zyx’ + zy’x

## Slide 46
F = zy’ (x’+X) + zyx + zyx’

## Slide 47
F = zy’ (x’+X) + zyx + zyx’

## Slide 48
F = zy’ (x’+X) + zy (x+X’)

## Slide 49
F = zy’ (x’+X) + zy (x+X’)

## Slide 50
F = zy’1 + zy1

## Slide 51
F = zy’ + zy

## Slide 52
F = z (y’+Y)

## Slide 53
F = z1

## Slide 54
F = z
0 gates!

## Slide 55
F = zy’x’ + zyx’ + Z’y’x
3 × 3-input-and
1 × 3-input-OR

## Slide 56
F = zy’x’ + zyx’ + Z’y’x

## Slide 57
F = zx’(y’+Y) + Z’y’x

## Slide 58
F = zx’ (y’+Y) + Z’y’x

## Slide 59
F = zx’1+ Z’y’x

## Slide 60
F = zx’+ Z’y’x
1 × 2-input-and
1 × 3-input-and
1 × 2-input-OR

## Slide 61
Minimization
Boolean Algebra (algebraically)
    Needs to be smart. It is hard due to guesswork (which rules to apply?)
    If the number of variables (ABCDEF…) and/or number of minterms (MAXTERMS) grows
    No Algorithm
    Is the result minimal?!

## Slide 62
Minimization
II) Map (Karnaugh map, K-map)
aka. Graphical Manipulation

## Slide 63
Minimization
II) Map (Karnaugh map, K-map)
aka. Graphical Manipulation
Algorithm; Straightforward, up to six variables
Result is always minimal

## Slide 64
Truth table
Y | X | F
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?

## Slide 65
Boolean function
Fsop = Σ minterms
Fpos = ∏ MAXTERMs
Algebraic Expression

## Slide 66
Logic circuit

## Slide 67
Maurice Karnaugh
Physicist
Mathematician
Inventor
Bell Labs (1954)
"The Map Method for Synthesis of
Combinational Logic Circuits”

## Slide 68
KARNAUGH MAP
/ˈkɑːrnɔː/

## Slide 69
1-Variable KARNAUGH MAP

## Slide 70
X | F
0 | m0
1 | m1
X | 
0 | 1
m0 | m1

## Slide 71
2-Variable KARNAUGH MAP

## Slide 72
Y | X | F
0 | 0 | m0
0 | 1 | m1
1 | 0 | m2
1 | 1 | m3
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3

## Slide 73
Y | X | F
0 | 0 | m0
0 | 1 | m1
1 | 0 | m2
1 | 1 | m3
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3

## Slide 74
Y | X | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
F(Y,X) = m0 = Y’X’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 0
 | 1 | 0 | 0
F(Y,X) = Y’X’ |  |  | 

## Slide 75
Y | X | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
F(Y,X) = m1 = Y’X |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 1
 | 1 | 0 | 0
F(Y,X) = Y’X |  |  | 

## Slide 76
Y | X | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m2 = YX’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 0
 | 1 | 1 | 0
F(Y,X) = YX’ |  |  | 

## Slide 77
Y | X | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
F(Y,X) = m3 = YX |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 0
 | 1 | 0 | 1
F(Y,X) = YX |  |  | 

## Slide 78
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
F(Y,X) = m0 + m1 F(Y,X) = Y’X’ + Y’X F(Y,X) = Y’(X’ + X) F(Y,X) = Y’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 0 | 0
F(Y,X) = Y’ |  |  | 

## Slide 79
Y | X | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
F(Y,X) = m2 + m3 F(Y,X) = YX’ + YX F(Y,X) = Y(X’ + X) F(Y,X) = Y |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 0
 | 1 | 1 | 1
F(Y,X) = Y |  |  | 

## Slide 80
Y | X | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
F(Y,X) = m1 + m3 F(Y,X) = Y’X + YX F(Y,X) = X(Y’ + Y) F(Y,X) = X |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 1
 | 1 | 0 | 1
F(Y,X) = X |  |  | 

## Slide 81
Y | X | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m0 + m2 F(Y,X) = Y’X’ + YX’ F(Y,X) = X’(Y’ + Y) F(Y,X) = X’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 0
 | 1 | 1 | 0
F(Y,X) = X’ |  |  | 

## Slide 82
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m0 + m1 + m2 F(Y,X) = Y’X’ + Y’X + YX’ F(Y,X) = Y’(X’ + X) + YX’ F(Y,X) = Y’ + YX’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 1 | 0
F(Y,X) = Y’ + YX’

## Slide 83
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m0 + m1 + m2 F(Y,X) = Y’X’ + Y’X + YX’ F(Y,X) = X’(Y’ + Y) + Y’X F(Y,X) = X’ + Y’X |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 1 | 0
F(Y,X) = X’ + Y’X

## Slide 84
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m0 + m1 + m2 F(Y,X) = Y’X’ + Y’X + YX’ F(Y,X) = Y’X’ + Y’X’ + Y’X + YX’ F(Y,X) = Y’(X’ + X) + Y’X’ + YX’ F(Y,X) = Y’ + Y’X’ + YX’ F(Y,X) = Y’ + X’(Y’ + Y) F(Y,X) = Y’ + X’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 1 | 0
F(Y,X) = Y’ + X’

## Slide 85
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
F(Y,X) = m0 + m1 + m2 + m3 F(Y,X) = Y’X’ + Y’X + YX’ + YX F(Y,X) = Y’(X’ + X) + Y(X’ + X) F(Y,X) = Y’ + Y F(Y,X) = 1 |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 1 | 1
F(Y,X) = m0+m1+m2+m3
F(Y,X) = 1

## Slide 86
Y | X | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m1 + m2 F(Y,X) = Y’X + YX’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 1
 | 1 | 1 | 0
F(Y,X) = m1 + m2 F(Y,X) = Y’X + YX’ |  |  | 

## Slide 87
Y | X | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
F(Y,X) = m0 + m2 F(Y,X) = Y’X’ + YX |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 0
 | 1 | 0 | 1
F(Y,X) = m0 + m2 F(Y,X) = Y’X’ + YX |  |  | 

## Slide 88
3-Variable KARNAUGH MAP

## Slide 89
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 90
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 91
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
Y

## Slide 92
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
Y'

## Slide 93
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
X

## Slide 94
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
X’ ?

## Slide 95
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 96
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  |  |  | 
 |  | 00 | 01 | 11 | 10 |  | 
Z | 0 | m0 | m1 | m3 | m2 | 0 | Z
 | 1 | m4 | m5 | m7 | m6 | 1 | 
X’
X’

## Slide 97
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?

## Slide 98
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’ +

## Slide 99
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’ + ZY

## Slide 100
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’ + Y

## Slide 101
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Y,X) = Π M(4,5)
F(Y,X) = (Z’+Y+X) (Z’+Y+X’)
F(Y,X) = ?
F(Y,X) = Π M(4,5)
F(Y,X) = ?

## Slide 102
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
F(Y,X) = Π M(4,5)
F(Y,X) = (Z’+Y+X) (Z’+Y+X’)
F(Y,X) = ?
F’(Y,X) = ∑ m(4,5)
F’(Y,X) = ZY’

## Slide 103
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Y,X) = Π M(4,5)
F(Y,X) = (Z’+Y+X) (Z’+Y+X’)
F(Y,X) = ?
F(Y,X) = Π M(4,5)
F(Y,X) = (F’)’
F(Y,X) = (ZY’)’
F(Y,X) = Z’+Y

## Slide 104
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?
F(Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’ + Y
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Y,X) = Π M(4,5)
F(Y,X) = (F’)’
F(Y,X) = (ZY’)’
F(Y,X) = Z’+Y
F(Y,X) = Π M(4,5)
F(Y,X) = (Z’+Y+X) (Z’+Y+X’)
F(Y,X) = ?

## Slide 105
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
F(Y,X) = ∑ m(0,2,4, 6)
F(Y,X) = Z’Y’X’+Z’YX’+ZY’X’+ZYX’
F(Y,X) = ?

## Slide 106
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
F(Y,X) = ∑ m(0,2,4, 6)
F(Y,X) = Z’Y’X’+Z’YX’+ZY’X’+ZYX’
F(Y,X) = ?
F(Y,X) = ∑ m(0,2,4, 6)
F(Y,X) = X’

## Slide 107
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
F(Z,Y,X) = Π M(1,3,5,7)
F(Y,X) = (Z+Y+X’)(Z+Y’+X’)(Z’+Y+X’)(Z’+Y’+X’)
F(Y,X) = ?
F(Z,Y,X) = Π M(1,3,5,7)
F(Y,X) = (X)’
F(Y,X) = X’

## Slide 108
4-Variable KARNAUGH MAP