## Slide 1
2001: A Space Odyssey (Stanley Kubrick-1968)

## Slide 2
2020: A Digital Odyssey
Notes: https://www.pinterest.ca/pin/231302130841121655/

## Slide 3
Number Systems |
Number Systems | Logic Gates |
Number Systems | Logic Gates | Combinational Logic |
Number Systems | Logic Gates | Combinational Logic | Flip-Flops |
Number Systems | Logic Gates | Combinational Logic | Flip-Flops | Sequential Logic |
Number Systems | Logic Gates | Combinational Logic | Flip-Flops| Sequential Logic | Computer Systems
(12)10 → (1100)2

## Slide 4
Design a Computer System

## Slide 5
John von Neumann
(/vɒn ˈnɔɪmən/)
1903 –1957
Mathematician, Physicist, Computer Scientist, Engineer
Polymath
He integrated pure and applied sciences. He made major contributions to many fields, including:
Mathematics
Physics
Economics (game theory)
Computing
Statistics

## Slide 6
Algorithm
Data
Problems
Computer
Processor
Bus
Memory to Store
Data (Input, Output)
int a=1; int b=2; int c;
Instructions (Code)
c = a + b;

## Slide 7
von Neumann Architecture
Principles
  Data and instructions are both stored in the main memory
  The content of the memory is addressable by location (regardless of what is stored in that location)
  Instructions are executed sequentially unless the order is explicitly modified

## Slide 8
Computer
System
Computer
Processor
Bus
Memory to Store
Data (Input, Output)
int a=1; int b=2; int c;
Instructions (Code)
c = a + b;
Bus
Input/Output
Devices
scanf("%d", &a);
scanf("%d", &b);
printf("%d", c);
Bus
Permanent Storage
fprintf() fscanf() fread() fwrite() fseek()

## Slide 9
Memory to Store
Processor
I/O
Power
I/O
I/O

## Slide 10
Memory to Store
Processor
I/O
Power
I/O
I/O

## Slide 11
Design Processor
Do Calculation

## Slide 12
Design Processor
Calculation on Data → Calculation on Numbers

## Slide 13
Design Processor
Number → Binary

## Slide 14
Computer
Processor
Bus
Memory to Store
Data (Input, Output)
int a=1; int b=2; int c;
Instructions (Code)
c = a + b;
We instruct the processor what to do!
Write instructions (programs)
Processor does our instructions

## Slide 15
Design Processor
Instruction Set
Cannot instruct a processor to do whatever we want!
Any processors have limitations.
  Some can only do addition,
  Some can do both addition and subtraction, but no division

## Slide 16
https://www.intel.com/content/dam/www/public/us/en/documents/manuals/64-ia-32-architectures-software-developer-instruction-set-reference-manual-325383.pdf
Notes: https://www.intel.com/content/dam/www/public/us/en/documents/manuals/64-ia-32-architectures-software-developer-instruction-set-reference-manual-325383.pdf

## Slide 17
Design Processor
Assembly Language
Writing programs using the Instruction Set of a particular processor
RISC (/rɪsk/): Reduced Instruction Set Computer
CISC (/ˈsɪsk/): Complex Instruction Set Computer

## Slide 18
Design Processor
RISC
Small but highly optimized set of instructions
e.g., integer calculation
https://en.wikipedia.org/wiki/Reduced_instruction_set_computer

## Slide 19
Design Processor
CISC
Large and NOT highly optimized set of instructions
e.g., integer and floating-point calculations
https://en.wikipedia.org/wiki/Complex_instruction_set_computer

## Slide 20
Current Processors
x86, x64
By Intel and AMD
instruction set size: ~981
How Many x86-64 Instructions Are There Anyway?

## Slide 21
Human Natural Language | Type | Example
High Level Programing Language | Imperative (What) | SQL SELECT * FROM Students
Middle Level Programming Language | Declarative (What + How) | C, C++, Java, Python int a = 1; a = a + 1;
Low Level Programming Language (Assembly Language) |  | Assembly x86, Assembly Z80 MOV 1, AX INC AX
Binary Digits (Machine Language) |  | 00010011 00001011

## Slide 22
Human Natural Language | Type | Example
High Level Programing Language | Imperative (What) | SQL SELECT * FROM Students
Middle Level Programming Language | Declarative (What + How) | C, C++, Java, Python int a = 1; a = a + 1;
Low Level Programming Language (Assembly Language) |  | Assembly x86, Assembly Z80 MOV 1, AX INC AX
Binary Digits (Machine Language) |  | 00010011 00001011
Compilers
Interpreters

## Slide 23
C/C++
Hossein’s Computer

## Slide 26
Memory Addresses
To see the actual binary machine language (OP Code) for each instruction,
open your executable file that the compiler makes. E.g., *.exe in Windows systems.

## Slide 28
Program vs. Process
Program: dead body of the instructions stored in permanent place (flash drive, ssd, hard disk, paper!)
Process: live body of the instructions stored in memory, ready to be fetched by the Processor and be executed!

## Slide 29
Program vs. Process
Process
Load into Memory
(Run)
Program
Finished/Killed
C, C++, Java, Python int a = 1; a = a + 1;
Assembly x86, Assembly Z80 MOV 1, AX INC AX
00010011 00001011
00010011 00001011
00010011 00001011
00010011 00001011

## Slide 30
Compilers vs. Interpreters
Instruction Encoders
Process
Load into Memory
(Run)
Program
Finished/Killed
C, C++, Java, Python int a = 1; a = a + 1;
Assembly x86, Assembly Z80 MOV 1, AX INC AX
00010011 00001011
int a = 1;  00010011 a = a + 1;  00001011
Compilers
Interpreters

## Slide 31
Instruction | Operation Code (OP Code)
c = a + b | 000 XXXX YYYY ZZZZ
c = a – b | 001 XXXX YYYY ZZZZ
c = a / b | 010 XXXX YYYY ZZZZ
c = a * b | 011 XXXX YYYY ZZZZ
c = {number} | 100 XXXX XXX XXXX
… | …
Instruction Encoders
very simplified version!

## Slide 32
Design Processor
Processor can only see binary-coded instructions
Processor only understand machine language
Instruction Set →Instruction Decoder

## Slide 33
Operation Code (OP Code) | What to do?
000 XXXX YYYY ZZZZ | Fetch the first operand from memory at XXXX address Store the first operand inside somewhere (AX) Fetch the second operand from memory at YYYY address Store the first operand inside somewhere else (BX) Use the n-bit Adder to add AX and BX Store the result inside somewhere else (CX) Push CX to memory at ZZZZ address
001 XXXX YYYY ZZZZ | 
010 XXXX YYYY ZZZZ | 
011 XXXX YYYY ZZZZ | 
100 XXXX XXX XXXX | 
… | 
Instruction Decoder
very simplified version!

## Slide 34
Operation Code (OP Code) | What to do?
000 XXXX YYYY ZZZZ | Fetch the first operand from memory at XXXX address Store the first operand inside somewhere (AX) Fetch the second operand from memory at YYYY address Store the first operand inside somewhere else (BX) Use the n-bit Adder to add AX and BX Store the result inside somewhere else (CX) Push CX to memory at ZZZZ address
001 XXXX YYYY ZZZZ | 
010 XXXX YYYY ZZZZ | 
011 XXXX YYYY ZZZZ | 
100 XXXX XXX XXXX | 
… | 
Instruction Decoder
very simplified version!

## Slide 35
Registers
Operand 1
Operand 2
Result
Internal Data Bus
Arithmetic
Logic
Data Bus
Internal Clock
Control
Control Bus
Address Bus
Internal Control Bus

## Slide 36
Data Bus
City
- Streets
1-way
2-way
- Gates
- Bridges
- Warehouses
- Policing
Control Bus
Address Bus
Registers
Operand 1
Operand 2
Result
Internal Data Bus
Arithmetic
Logic
Internal Clock
Control
Internal Control Bus

## Slide 37
Registers
Operand 1
Operand 2
Result
Internal Data Bus
Arithmetic
Logic
Data Bus
City
- Streets
1-way
2-way
- Gates
- Bridges
- Warehouses
- Policing
Internal Clock
Control
Control Bus
Address Bus
Internal Control Bus

## Slide 38
Registers
Some vectors of FFs

## Slide 39
Instruction Pointer (IP)
aka. Program Counter (PC), Instruction Address Register (IAR), Instruction Counter
Keep track of the address of next instruction in memory

## Slide 40
Instruction Pointer (IP)
Keep track of the address of next instruction in memory
Why is it called ‘counter’?
aka. Program Counter (PC), Instruction Address Register (IAR), Instruction Counter

## Slide 41
Address | Memory | High Level Instr.
0000 | 100 0111 0001 0000 | int a = 1;
0001 | 100 1000 0010 0000 | int b = 2; Current Instruction
0010 | 100 1001 0000 0000 | int c;
0011 | 001 0111 1000 1001 | c = a + b;
0100 | … | 
… | …. | 
Address Bus
Where is the next instruction to be fetched and execute?

## Slide 42
Address Bus
In von Neumann architecture, instructions are executed sequentially!
So, the next would be the address of current + 1
Address | Memory | High Level Instr.
0000 | 100 0111 0001 0000 | int a = 1;
0001 | 100 1000 0010 0000 | int b = 2; Current Instruction
0010 | 100 1001 0000 0000 | int c;
0011 | 001 0111 1000 1001 | c = a + b;
0100 | 100 0111 0001 0000 | …
… | …. | …

## Slide 43
Instruction Pointer (IP)
We already designed a 3-bit counter
00, 01, 10, 11
aka. Program Counter (PC), Instruction Address Register (IAR), Instruction Counter

## Slide 44
Instruction Pointer (IP)
IP is a n-bit counter. What is n?
aka. Program Counter (PC), Instruction Address Register (IAR), Instruction Counter

## Slide 45
Instruction Pointer (IP)
IP is a n-bit counter. What is n?
IP contains a memory address.
Address bus contains a memory address at a time.
So, IP is the same size as address bus. Here, 4-bit address bus, we have 4-bit IP.
aka. Program Counter (PC), Instruction Address Register (IAR), Instruction Counter

## Slide 46
Where is the current instruction?

## Slide 47
Instruction Register (IR or IX)
Holds the current instruction that is fetched from memory and is just about to be executed.
As soon as the instruction placed in IR, the processor starts executing the instruction and IP++ to point to the next instruction to be executed next.

## Slide 48
Address Bus
Address | Memory | High Level Instr.
0000 | 100 0111 0001 0000 | int a = 1;
0001 | 100 1000 0010 0000 | int b = 2; Current Instruction
0010 | 100 1001 0000 0000 | int c;
0011 | 001 0111 1000 1001 | c = a + b;
0100 | 100 0111 0001 0000 | …
… | …. | …
IX=100 1000 0010 0000
IP=0010

## Slide 49
Address Bus
0010
Address | Memory | High Level Instr.
0000 | 100 0111 0001 0000 | int a = 1;
0001 | 100 1000 0010 0000 | int b = 2; Current Done!
0010 | 100 1001 0000 0000 | int c;
0011 | 001 0111 1000 1001 | c = a + b;
0100 | 100 0111 0001 0000 | …
… | …. | …
IX=100 1000 0010 0000
IP=0010
1) Load address bus with IP

## Slide 50
Address Bus
0010
Address | Memory | High Level Instr.
0000 | 100 0111 0001 0000 | int a = 1;
0001 | 100 1000 0010 0000 | int b = 2; Current Done!
0010 | 100 1001 0000 0000 | int c;
0011 | 001 0111 1000 1001 | c = a + b;
0100 | 100 0111 0001 0000 | …
… | …. | …
IX=100 1000 0010 0000
IP=0010
2) Load control bus to read from memory
Control Bus
C=0 (Read)

## Slide 51
Address Bus
0010
Address | Memory | High Level Instr.
0000 | 100 0111 0001 0000 | int a = 1;
0001 | 100 1000 0010 0000 | int b = 2; Current Done!
0010 | 100 1001 0000 0000 | int c;
0011 | 001 0111 1000 1001 | c = a + b;
0100 | 100 0111 0001 0000 | …
… | …. | …
IX=100 1001 0000 0000
IP=0010
3) Read data bus and load it into IX
Control Bus
C=0 (Read)
Data Bus
100 1001 0000 0000

## Slide 52
Address Bus
Address | Memory | High Level Instr.
0000 | 100 0111 0001 0000 | int a = 1;
0001 | 100 1000 0010 0000 | int b = 2; Current Done!
0010 | 100 1001 0000 0000 | int c;
0011 | 001 0111 1000 1001 | c = a + b;
0100 | 100 0111 0001 0000 | …
… | …. | …
IX= 100 1001 0000 0000
IP=0011
4) Increment IP
Control Bus
Data Bus

## Slide 53
Instruction Register (IR or IX)
n-bit Register. What is n?

## Slide 54
Fetch Instruction Cycle
Load address bus with IP
Load control bus to read from memory
Read data bus and load it into IX
Increment IP

## Slide 55
Memory Address Register (MAR)
Holds the address of memory location to Read/Write data from.

## Slide 56
Memory Data Register (MDR)
Holds the actual value that is either
Read from memory, or
To be written to memory

## Slide 57
Memory Address Register (MAR)
Memory Data Register (MDR)
Work hand-in-hand to facilitate the communication of the processor and the main memory
What are their sizes?

## Slide 58
Address Bus
Address | Memory | High Level Instr.
0000 | 100 0111 0001 0000 | int a = 1;
0001 | 100 1000 0010 0000 | int b = 2; Current Done!
0010 | 100 1001 0000 0000 | int c;
0011 | 001 0111 1000 1001 | c = a + b;
0100 | 100 0111 0001 0000 | …
… | …. | …
IX=001 0111 1000 1001
IP=0100
What are the steps to execute this instruction?
Control Bus
Data Bus

## Slide 59
Fetch the first operand from memory
  Load MAR with the address of ‘a’ from the instruction op code
  Load address bus with MAR
  Load control bus with C=0 (Read)
  Load MDR with the content of data bus
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;
0100 |  | 
0101 |  | 
0110 |  | 
0111 | 000 0000 0000 0001 | 
IX= 001 0111 1000 1001
Address Bus
Control Bus
Data Bus
MAR=0111
MDR=000 0000 0000 0001

## Slide 60
2) Fetch the second operand from memory
  Load MAR with the address of ‘b’ from the instruction op code
  Load address bus with MAR
  Load control bus with C=0 (Read)
  Load MDR with the content of data bus
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;
0100 |  | 
0101 |  | 
0110 |  | 
0111 | 000 0000 0000 0001 | 
1000 | 000 0000 0000 0010 | 
IX= 001 0111 1000 1001
Address Bus
Control Bus
Data Bus
MAR=1000
MDR=000 0000 0000 0010

## Slide 61
2) Fetch the second operand from memory
  Load MAR with the address of ‘b’ from the instruction op code
  Load address bus with MAR
  Load control bus with C=0 (Read)
  Load MDR with the content of data bus. Wait! I lost the value of ‘a’ inside the processor!
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;
0100 |  | 
0101 |  | 
0110 |  | 
0111 | 000 0000 0000 0001 | 
1000 | 000 0000 0000 0010 | 
Address Bus
Control Bus
Data Bus
IX= 001 0111 1000 1001
MAR=1000
MDR=000 0000 0000 0010

## Slide 62
2) Fetch the second operand from memory
  Move MDR (value of ‘a’) to somewhere (AX) first!
  Load MAR with the address of ‘b’ from the instruction op code
  Load address bus with MAR
  Load control bus with C=0 (Read)
  Load MDR with the content of data bus.
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;
0100 |  | 
0101 |  | 
0110 |  | 
0111 | 000 0000 0000 0001 | 
1000 | 000 0000 0000 0010 | 
Address Bus
Control Bus
Data Bus
IX= 001 0111 1000 1001
MAR=1000
MDR=000 0000 0000 0010

## Slide 63
3) Use the n-bit Adder to add AX and MDR
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;
AX= 000 0000 0000 0001
MDR=000 0000 0000 0010

## Slide 64
4) Store the result somewhere. Where?
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;
AX= 000 0000 0000 0001
MDR=000 0000 0000 0010

## Slide 65
4) Store the result somewhere. Where?
We want to write it back to memory at location for ‘c’
So, better to store it in MDR
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;
AX= 000 0000 0000 0001
MDR=000 0000 0000 0010

## Slide 66
4) Store the result somewhere. Where?
What do we want to do next?
We want to write it back to memory at location for ‘c’
So, better to store it in MDR
AX= 000 0000 0000 0001
MDR=000 0000 0000 0011
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;

## Slide 67
Address Bus
1001
Control Bus
1
Data Bus
000 0000 0011
5) Write the result back to memory at location for ‘c’.
  Find the address of ‘c’ in op code
  Load it into MAR
  Load address bus with MAR
  Load data bus with MDR
  Load control bus with C=1 (Write)
MDR=000 0000 0011
Address | Memory | High Level Instr.
0011 | 001 0111 1000 1001 | c = a + b;
 | … | 
1001 | 000 0000 0000 0011 | 
IX= 001 0111 1000 1001
MAR= 1001

## Slide 68
Accumulator (AX)
This is the most frequently used register.
Any intermediate results
somewhere  AX

## Slide 69
General Purpose Registers
R1, R2, …, Ri

## Slide 72
Arithmetic & Logic Unit
(ALU)

## Slide 73
Arithmetic Unit
Integer Arithmetic (Addition, Subtraction)
- Multiplication: multiple addition
- Division: multiple subtraction
Floating Point Arithmetic (FPU)

## Slide 74
Logic Unit
Bitwise
AND, OR, XOR, 1’s Comp.

## Slide 75
Recap
Fetch Instruction Cycle
Execution Cycle
  Depends on OP Code
    Arithmetic
    Logic

## Slide 76
Memory to Store
Processor
I/O
Power
I/O
I/O

## Slide 77
Microprocessor
Central Processing Unit (CPU)
Intel (Xeon), AMD (Ryzen)
Graphic Processing Unit (GPU)
nVidia (GeForce) for Video Card (Gaming)
AI Acceleration (Neural Nets)
Tensor Processing Unit (TPU)
Google (TensorFlow AI Lib for Neural Nets)

## Slide 78
COMP-2660
Computer Architecture II
Microprocessor Programming

## Slide 79
Postscript
Office Hours Before Week
- Practice on questions
Office Hours Final Exam
- Review exam questions