## Slide 1
Design
a design algorithm for any digital units (logic circuits), given truth table

## Slide 2
minterm
aka. Standard Product

## Slide 3
X’ vs. x
1 binary variable appear either:
in its normal form X, or
in its complement form X’

## Slide 4
m0 | X’
m1 | X

## Slide 5
YX vs. YX’ vs. Y’x vs. Y’X’
2 binary variables appear either in one of these forms:

## Slide 6
m0 | Y’X’
m1 | Y’X
m2 | YX’
m3 | YX

## Slide 7
ZYX vs. ZYX’ vs. …
3 binary variables appear either in one of these forms: how many?

## Slide 8
ZYX vs. ZYX’ vs. …
3 binary variables appear either in one of these forms: how many?
Each variable can take 2 forms (normal and complement)
We have 3 variables, 2×2×2 = 23 = 8

## Slide 9
m0 | Z’Y’X’
m1 | Z’Y’X
m2 | Z’YX’
m3 | Z’YX
m4 | ZY’X’
m5 | ZY’X
m6 | ZYX’
m7 | ZYX

## Slide 10
An-1…A2A1A0 vs. An-1…A2A1A’0 …
n binary variables appear either in one of these forms: how many?
Each variable can take 2 forms (normal and complement)
We have n variables, 2×2×2× … ×2 = 2n

## Slide 11
m0 | A’n-1…A’2A’1A’0
m1 | A’n-1…A’2A’1A0
m2 | A’n-1…A’2A1A’0
… | …
… | …
m2n-3 | An-1…A2A’1A0
m2n-2 | An-1…A2A1A’0
m2n-1 | An-1…A2A1A0

## Slide 12
Truth table
en.wikipedia.org/wiki/Truth_table

## Slide 13
X | F = F(X) = ?
0 | ?
1 | ?

## Slide 14
X | F = F(X) = 0
0 | 0
1 | 0

## Slide 15
X | F = F(X) =1
0 | 1
1 | 1

## Slide 16
X | F = F(X) = X’
0 | 1
1 | 0

## Slide 17
m0 | X’
m1 | X

## Slide 18
X | F = F(X) = X’ = m0
0 | 1
1 | 0

## Slide 19
X | F = F(X) = X’ = m0
0 | 1
1 | 0

## Slide 20
X
F = X’=m0

## Slide 21
X | F = F(X) = X
0 | 0
1 | 1

## Slide 22
X | F = F(X) = X = m1
0 | 0
1 | 1

## Slide 23
X | F = F(X) = X = m1
0 | 0
1 | 1

## Slide 24
X
F = X=m1
Digital Buffer
X
X’
X

## Slide 25
Truth table ↔ minterm

## Slide 26
Y | X | F = F(Y,X) = ?
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?

## Slide 27
Y | X | F = F(Y,X) = 0
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 28
Y | X | F = F(Y,X) = YX
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 29
X
F = YX = m3
Y

## Slide 30
m0 | Y’X’
m1 | Y’X
m2 | YX’
m3 | YX

## Slide 31
Y | X | F = F(Y,X) = YX =m3
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 32
Y | X | F = F(Y,X) = YX =m3
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 33
Y | X | F = F(Y,X) = YX’ =m2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0

## Slide 34
Y | X | F = F(Y,X) = YX’ =m2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0

## Slide 35
X
F = YX’ = m2
Y

## Slide 36
Y | X | F = F(Y,X) = Y’X =m1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 37
Y | X | F = F(Y,X) = Y’X =m1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 38
X
F = Y’X=m1
Y

## Slide 39
Y | X | F = F(Y,X) = Y’X’ =m0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 40
Y | X | F = F(Y,X) = Y’X’ =m0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 41
X
F = Y’X’=m0
Y

## Slide 42
Y | X | F = F(Y,X) = ?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 43
Y | X | F = F(Y,X) = Y’X’
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 44
Y | X | F = F(Y,X) = Y’X’+Y’X
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 45
Y | X | F = F(Y,X) = m0+m1
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 46
Y | X | F = F(Y,X) = ∑m(0,1)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 47
X
Y
Y’X’
Y’X
Y’X’+Y’X

## Slide 48
X
Y
Y’X’
Y’X
Y’X’+Y’X

## Slide 49
Y | X | F = F(Y,X) = ?
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 50
Y | X | F = F(Y,X) = Y’X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 51
Y | X | F = F(Y,X) = m1+m2
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 52
Y | X | F = F(Y,X) = ∑m(1,2)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 53
X
Y
Y’X
YX’
Y’X+YX’
X
Y

## Slide 54
Y | X | F = F(Y,X) = Y’X+YX’ = m1+m2
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
X
Y
Y+X
Exclusive-OR (XOR)

## Slide 55
Y | X | F = F(Y,X) = ?
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 56
Y | X | F = F(Y,X) = Y’X’
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 57
Y | X | F = F(Y,X) = Y’X’+YX
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 58
Y | X | F = F(Y,X) = m0+m3
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 59
Y | X | F = F(Y,X) = ∑m(0,3)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 60
X
Y
Y’X’
YX
Y’X’+YX
X
Y

## Slide 61
Y | X | F = F(Y,X) = Y’X’+YX = m0+m3
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X
Y
Y X
NOT Exclusive-OR (XNOR)

## Slide 62
Y | X | F = F(Y,X) = ?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 63
Y | X | F = F(Y,X) = Y’X’
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 64
Y | X | F = F(Y,X) = Y’X’+Y’X
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 65
Y | X | F = F(Y,X) = Y’X’+Y’X+YX
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 66
Y | X | F=F(Y,X)=m0+m1+m3 =∑m(0,1,3)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 67
X
Y
Y’X’
Y’X
Y’X’+Y’X+YX
X
Y
YX

## Slide 68
SUM OF PRODUCTS
(SOP)

## Slide 69
X
Y
Y’X’
Y’X
Y’X’+Y’X+YX
X
Y
YX

## Slide 70
2 LEVELS
AND  OR

## Slide 71
X
Y
Y’X’
Y’X
Y’X’+Y’X+YX
X
Y
YX

## Slide 72
Given 3 inputs, design a circuit to determine if there is even number of 1

## Slide 73
Truth table ↔ minterm

## Slide 74
INPUTS/Binary Variables
OUTPUTS/Boolean Functions

## Slide 75
Z | Y | X | F(Z,Y,X)=?
0 | 0 | 0 | ?
0 | 0 | 1 | ?
0 | 1 | 0 | ?
0 | 1 | 1 | ?
1 | 0 | 0 | ?
1 | 0 | 1 | ?
1 | 1 | 0 | ?
1 | 1 | 1 | ?

## Slide 76
Z | Y | X | F(Z,Y,X)=?
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 77
Z | Y | X | F(Z,Y,X)=Z’Y’X’
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 78
Z | Y | X | F(Z,Y,X)=Z’Y’X’+Z’YX
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 79
Z | Y | X | F(Z,Y,X)=Z’Y’X’+Z’YX+ZY’X
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 80
Z | Y | X | F(Z,Y,X)=Z’Y’X’+Z’YX+ZY’X+ZYX’
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 81
Z | Y | X | F(Z,Y,X)=m0+m3+m5+m6
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 82
Z | Y | X | F(Z,Y,X)=m0+m3+m5+m6=∑m(0,3,5,6)
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 83
X
Y
Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z

## Slide 84
SUM OF PRODUCTS (SOP)
2 LEVELS AND-OR

## Slide 85
X
Y
Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z

## Slide 86
X
Y
Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z

## Slide 87
Show the remainder (MOD)
number % 3 = ?

## Slide 88
Truth table ↔ minterm

## Slide 89
INPUTS/Binary Variables
OUTPUTS/Boolean Functions

## Slide 90
What is the range of numbers?

## Slide 91
What is the range of numbers?
[0, 15]10

## Slide 92
How many input binary variables?
[0, 15]10 = [0,1111]2 = [0000,1111]2

## Slide 93
W | Z | Y | X
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1

## Slide 94
What is the range of output?

## Slide 95
What is the range of output?
The remainder of any number divided by 3 is 0, 1, 2

## Slide 96
What is the range of output?
[0, 2]10

## Slide 97
How many Boolean function?
[0, 2]10 = [0, 10]2 = [00, 10]2

## Slide 98
W | Z | Y | X | F1 | F2
0 | 0 | 0 | 0 |  | 
0 | 0 | 0 | 1 |  | 
0 | 0 | 1 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 |  | 
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 

## Slide 99
W | Z | Y | X | F1 | F2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 |  | 
0 | 0 | 1 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 |  | 
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 

## Slide 100
W | Z | Y | X | F1 | F2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 |  | 
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 

## Slide 101
W | Z | Y | X | F1 | F2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 |  | 
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 

## Slide 102
W | Z | Y | X | F1 | F2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 |  | 
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 

## Slide 103
W | Z | Y | X | F1 | F2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0

## Slide 104
minterms

## Slide 105
W | Z | Y | X | F1=m2+m5+m8+m11+m14 | F2
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0

## Slide 106
W | Z | Y | X | F1=(2,5,8,11,14) | F2=m1+m4+m7+m10+m13
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0
W | Z | Y | X |  | F2=m1+m4+m7+m10+m13
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0

## Slide 107
W | Z | Y | X | F1=(2,5,8,11,14) | F2=(1,4,7,10,13)
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0
W | Z | Y | X |  | 
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0