## Slide 1
Universality

## Slide 2
Universal SET
Is it possible to implement ALL the possible Boolean functions using NOT, AND, OR, NAND, NOR? Yes!

## Slide 3
Universal SET
What if we are not given some!
What if some are very costly! E.g., NOT
Can we reduce this set? E.g., building NOT by NAND/ NOR

## Slide 4
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR
{NOT, OR} | If we could design AND
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 5
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR (a Complete Set)
{NOT, OR} | If we could design AND (a Complete Set)
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 6
Universal SET
{NOT, AND}

## Slide 7
De Morgan's laws
► (Y+X)’= Y’X’
    ((Y+X)’)’= (Y’X’)’
    Y+X= (Y’X’)’
Augustus De Morgan
(1806–1871)
Mathematician
Logician

## Slide 8
X
Y
X’
Y’
Y’X’=(Y+X)’
Y+X

## Slide 9
X
Y
Y+X
OR

## Slide 10
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR (a Complete Set)
{NOT, OR} | If we could design AND (a Complete Set)
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 11
Universal SET
{NOT, OR}

## Slide 12
De Morgan's laws
► Y’+X’ = (YX)’
  (Y’+X’)’ = ((YX)’)’
  (Y’+X’)’ = YX
Augustus De Morgan
(1806–1871)
Mathematician
Logician

## Slide 13
X
Y
X’
Y’
Y’+X’=(YX)’
YX

## Slide 14
X
Y
YX
AND

## Slide 15
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR (a Complete Set)
{NOT, OR} | If we could design AND (a Complete Set)
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 16
Universal GATE
{NAND}

## Slide 17
NOT ► (XX)’ = (X↑X) = X’
X
X’

## Slide 18
AND►NOT (NAND) = ((Y↑X))’=YX
X
(Y↑X)
Y
(Y↑X)’= YX

## Slide 19
OR ► DE Morgan's law
(Y+X)’ = Y’X’
((Y+X)’)’ = (Y’X’)’
Y + X = (Y’X’)’
Y + X = Y’ ↑ X’

## Slide 20
OR: DE Morgan's law
X
X’
Y
Y’
(Y’X’)’ =
Y+X =
Y’ ↑ X’

## Slide 21
https://commons.wikimedia.org/wiki/7400_series_overview

## Slide 22
X
X
X’
Y
Y
Y’
Y’
X’
Y+X

## Slide 23
Set | Universal set
{NOT, AND, OR, NAND, NOR} | Yes! (a Full Set)
{NOT, AND, OR} | Yes, (a Full Set) NAND = AND-NOT NOR = OR-NOT
{NOT, AND} | If we could design OR (a Complete Set)
{NOT, OR} | If we could design AND (a Complete Set)
{NOT} | If we could design AND, OR
{AND} | If we could design NOT, OR
{OR} | If we could design NOT, AND
{NAND} | If we could design NOT, AND, OR
{NOR} | If we could design NOT, AND, OR

## Slide 24
Universal GATE
{NOR}

## Slide 25
NOT ► (X+X)’ = (XX) = X’
OR ► NOT (NOR)
AND ► De Morgan's law
(Y’+X’)’ = YX = (Y’↓X’)

## Slide 27
https://commons.wikimedia.org/wiki/7400_series_overview

## Slide 28
X
X
X’
Y
Y
Y’
Y’
X’
YX

## Slide 29
Universal GATE
SoP  {NAND}

## Slide 30
F1=Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z
F2=ZY’X’+ZY’X

## Slide 31
X
Y
Z
F2=ZY’X’+ZY’X

## Slide 32
X
Y
Z
F2= m4+m5
F2= ((F2)’)’

## Slide 33
X
Y
Z
F2= m4+m5
F2= ((F2)’)’
F2= ((m4+m5)’)’

## Slide 34
X
Y
Z
F2= m4+m5
F2= ((F2)’)’
F2= ((m4+m5)’)’
F2= (m’4m’5)’

## Slide 35
X
Y
Z
F2= m4+m5
F2= ((F2)’)’
F2= ((m4+m5)’)’
F2= (m’4m’5)’
F2= ((ZY’X’)’ (ZY’X)’)’

## Slide 36
X
Y
Z
F2= m4+m5
F2= ((F2)’)’
F2= ((m4+m5)’)’
F2= (m’4m’5)’
F2= ((ZY’X’)’ (ZY’X)’)’
F2= ((Z↑Y’↑X’) (Z↑Y’↑X))’

## Slide 37
X
Y
Z
F2= m4+m5
F2= ((F2)’)’
F2= ((m4+m5)’)’
F2= (m’4m’5)’
F2= ((ZY’X’)’ (ZY’X)’)’
F2= ((Z↑Y’↑X’) (Z↑Y’↑X))’
F2= ((Z↑Y’↑X’)↑(Z↑Y’↑X))

## Slide 38
X
Y
Z
F2= ((Z↑Y’↑X’)↑(Z↑Y’↑X))

## Slide 39
F1=Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z

## Slide 40
F1=Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z
F1= ((F1)’)’

## Slide 41
F1=Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z
F1= ((F1)’)’
F1= ((m0+m3+m5+m6)’)’

## Slide 42
F1=Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z
F1= ((F1)’)’
F1= ((m0+m3+m5+m6)’)’
F1= (m’0 m’3 m’5 m’6)’

## Slide 43
F1=Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z
F1= ((F1)’)’
F1= ((m0+m3+m5+m6)’)’
F1= (m’0 m’3 m’5 m’6)’
F1= ((Z’Y’X’)’ (Z’YX)’ (ZY’X)’ (ZYX’)’)’

## Slide 44
F1=Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z
F1= ((F1)’)’
F1= ((m0+m3+m5+m6)’)’
F1= (m’0 m’3 m’5 m’6)’
F1= ((Z’Y’X’)’ (Z’YX)’ (ZY’X)’ (ZYX’)’)’
F1= ((Z’↑Y’↑X’) (Z’↑Y↑X) (Z↑Y’↑X) (Z↑Y↑X’))’

## Slide 45
F1=Z’Y’X’+Z’YX+ZY’X+ZYX’
X
Y
Z
F1= ((F1)’)’
F1= ((m0+m3+m5+m6)’)’
F1= (m’0 m’3 m’5 m’6)’
F1= ((Z’Y’X’)’ (Z’YX)’ (ZY’X)’ (ZYX’))’
F1= ((Z’↑Y’↑X’) (Z’↑Y↑X) (Z↑Y’↑X) (Z↑Y↑X’))’
F1= ((Z’↑Y’↑X’)↑(Z’↑Y↑X)↑(Z↑Y’↑X)↑(Z↑Y↑X’))

## Slide 46
X
Y
Z
F1= ((F1)’)’
F1= ((m0+m3+m5+m6)’)’
F1= (m’0 m’3 m’5 m’6)’
F1= ((Z’Y’X’)’ (Z’YX)’ (ZY’X)’ (ZYX’))’
F1= ((Z’↑Y’↑X’) (Z’↑Y↑X) (Z↑Y’↑X) (Z↑Y↑X’))’
F1= ((Z’↑Y’↑X’)↑(Z’↑Y↑X)↑(Z↑Y’↑X)↑(Z↑Y↑X’))

## Slide 47
X
Y
Z
F2= ((Z↑Y’↑X’)↑(Z↑Y’↑X))
F1= ((Z’↑Y’↑X’)↑(Z’↑Y↑X)↑(Z↑Y’↑X)↑(Z↑Y↑X’))

## Slide 48
X
Y
Z
F2= ((Z↑Y’↑X’)↑(Z↑Y’↑X))
F1= ((Z’↑Y’↑X’)↑(Z’↑Y↑X)↑(Z↑Y’↑X)↑(Z↑Y↑X’))
NOT by NAND?

## Slide 49
X
Y
Z
F2= ((Z↑Y’↑X’)↑(Z↑Y’↑X))
F1= ((Z’↑Y’↑X’)↑(Z’↑Y↑X)↑(Z↑Y’↑X)↑(Z↑Y↑X’))
NOT by NAND?

## Slide 50
Universal GATE {NAND}
F=(F’)’=(SoP’)’

## Slide 51
Universal GATE
{NOR}

## Slide 52
Universal GATE
PoS  {NOR}
FPoS = (F’)’
Lecture Assignment

## Slide 53
RECAP
Any Boolean Function F:
- Sum (OR) of Products (ANDs)
- Sum of minterms for Entries with 1
  - ANDs-OR
  - NAND via (F’)’
- Product (AND) of Sums (ORs)
- Product of MAXTERMS (NOT minterms) for Entries with 0
  - ORs-AND
  - NOR via (F’)’

## Slide 54
Universal GATE
SoP  {NAND}
SoP  {NOR} ?
PoS  {NOR}
PoS  {NAND} ?
Lecture Assignment