## Slide 1
Logic
Circuits
Sequential
Combinational

## Slide 3
Feedback

## Slide 4
Combinational Logic
Combination of logic gates on the present inputs → the outputs at any time!
A combinational circuit performs an operation that can be specified logically by a set of Boolean functions.
aka. Combinational Circuit

## Slide 5
Y
X
Time
X
F
Y
Voltage

## Slide 6
Y
X
Time
X
F
Y
Voltage
Propagation Delay (Gate Delay) ≈ Δt
https://en.wikipedia.org/wiki/Propagation_delay#Electronics

## Slide 7
Y
X
Time
X
F
Y
Voltage
Propagation Delay (Gate Delay) ≈ Δt ≈ 0
https://en.wikipedia.org/wiki/Propagation_delay#Electronics

## Slide 8
What we’ve done so far
Combinational Logic aka. Combinational Circuit

## Slide 9
Design a combinational logic circuit:
Truth Table (Inputs, Outputs)
Output Boolean Functions (SoP: ∑m | PoS: ∏M)
Minimization
  Algebraically | K-Map | Quine-McCluskey
Logic Diagram | Circuit

## Slide 10
Combinational
Logic
Coders
Data
Transmission
Arithmatic
&
Logical Op

## Slide 11
Data
Transmission
Decoder, Encoder
Multiplexer (MUX, MPX), De-Multiplexer (Demux)
Binary Adder, Binary Subtractor, Binary Multiplier
Binary Comparator (Magnitude Comparator)
Binary Codes (BCD, Excess-3, Gray)
Arithmatic
&
Logical Op
Coders

## Slide 12
Data
Transmission
Decoder, Encoder
Multiplexer (MUX, MPX), De-Multiplexer (Demux)
Binary Adder, Binary Subtractor, Binary Multiplier
Binary Comparator (Magnitude Comparator)
Binary Codes (BCD, Excess-3, Gray)
Arithmatic
&
Logical Op
Coders

## Slide 13
Coding

## Slide 14
A EncodeB

## Slide 15
A Decode B

## Slide 16
A ↔ [Enc][Dec]code ↔ B
By a convention
Math, e.g., conversion in radix numbering system
Non-math, e.g., in base-64, the value of characters
Engineering
etc

## Slide 17
1-way Coding
A Decode B
A Encode B

## Slide 18
A ↔ Look up Table ↔ B
2-way Coding

## Slide 19
A ↔ Look up Table ↔ B
Base-64

## Slide 20
Digit | Value |  | Digit | Value |  | Digit | Value |  | Digit | Value
A | 0 |  | Q | 16 |  | g | 32 |  | w | 48
B | 1 |  | R | 17 |  | h | 33 |  | x | 49
C | 2 |  | S | 18 |  | i | 34 |  | y | 50
D | 3 |  | T | 19 |  | j | 35 |  | z | 51
E | 4 |  | U | 20 |  | k | 36 |  | 0 | 52
F | 5 |  | V | 21 |  | l | 37 |  | 1 | 53
G | 6 |  | W | 22 |  | m | 38 |  | 2 | 54
H | 7 |  | X | 23 |  | n | 39 |  | 3 | 55
I | 8 |  | Y | 24 |  | o | 40 |  | 4 | 56
J | 9 |  | Z | 25 |  | p | 41 |  | 5 | 57
K | 10 |  | a | 26 |  | q | 42 |  | 6 | 58
L | 11 |  | b | 27 |  | r | 43 |  | 7 | 59
M | 12 |  | c | 28 |  | s | 44 |  | 8 | 60
N | 13 |  | d | 29 |  | t | 45 |  | 9 | 61
O | 14 |  | e | 30 |  | u | 46 |  | + | 62
P | 15 |  | f | 31 |  | v | 47 |  | / | 63

## Slide 21
A ↔ Look up Table ↔ Binary Number
Binary Codes
Assigning binary numbers to things

## Slide 22
Binary Coded Decimal
BCD (8421)
Decimal ↔ Look up Table ↔ Binary Number

## Slide 24
Decimal | BCD (Binary Code) | Binary Number
10 | 0001 0000 | 0000 1010
11 | 0001 0001 | 0000 1011
12 | 0001 0010 | 0000 1100
13 | 0001 0011 | 0000 1101
14 | 0001 0100 | 0000 1110
15 | 0001 0101 | 0000 1111
16 | 0001 0110 | 0001 0000
17 | 0001 0111 | 0001 0001
18 | 0001 1000 | 0001 0010
19 | 0001 1001 | 0001 0011
20 | 0010 0000 | 0001 0100
21 | 0010 0001 | 0001 0101
22 | 0010 0010 | 0001 0110
23 | 0010 0011 | 0001 0111
… | … | …

## Slide 25
Decimal | BCD (Binary Code) | Binary Number
10 | 0001 0000 | 0000 1010
11 | 0001 0001 | 0000 1011
12 | 0001 0010 | 0000 1100
13 | 0001 0011 | 0000 1101
14 | 0001 0100 | 0000 1110
15 | 0001 0101 | 0000 1111
16 | 0001 0110 | 0001 0000
17 | 0001 0111 | 0001 0001
18 | 0001 1000 | 0001 0010
19 | 0001 1001 | 0001 0011
20 | 0010 0000 | 0001 0100
21 | 0010 0001 | 0001 0101
22 | 0010 0010 | 0001 0110
23 | 0010 0011 | 0001 0111
… | … | …

## Slide 26
(185)10 = (?)BCD = (?)2

## Slide 27
(185)10 = (0001)BCD = (?)2

## Slide 28
(185)10 = (0001 1000)BCD = (?)2

## Slide 29
(185)10 = (0001 1000 0101)BCD = (?)2

## Slide 30
(185)10 = (0001 1000 0101)BCD = (?)2

## Slide 31
(185)10 = (0001 1000 0101)BCD = (?)2
 | Remainder
185÷2 | 1
92÷2 | 0
46÷2 | 0
23÷2 | 1
11÷2 | 1
5÷2 | 1
2÷2 | 0
1÷2 | 1
0 | 

## Slide 32
(185)10 = (0001 1000 0101)BCD = (10111001)2

## Slide 33
A ↔ Look up Table ↔ B
Other Binary Codes

## Slide 34
Aiken

## Slide 35
Other Binary Codes
Aiken (2421)
/ˈeɪkən/
https://en.wikipedia.org/wiki/Aiken_code

## Slide 36
Howard Hathaway Aiken
(March 8, 1900 – March 14, 1973)
Physicist
Pioneer in computing
Original conceptual designer behind IBM's Harvard Mark I
Notes: The Aiken code differs from the standard 8421 BCD code in that the Aiken code does not weight the fourth digit as 8 as with the standard BCD code but with 2.

## Slide 37
Aiken
NOT

## Slide 38
(185)10 = (0001 1000 0101)BCD (8421)
(185)10 = (10111001)2
(185)10 = (0001 NOT(1) NOT(4))Aiken (2421)

## Slide 39
(185)10 = (0001 1000 0101)BCD (8421)
(185)10 = (10111001)2
(185)10 = (0001 NOT(0001) NOT(0100))Aiken (2421)

## Slide 40
(185)10 = (0001 1000 0101)BCD (8421)
(185)10 = (10111001)2
(185)10 = (0001 1110 1011)Aiken (2421)

## Slide 41
Other Binary Codes
Excess-3 (XS-3)
https://en.wikipedia.org/wiki/Excess-3

## Slide 42
George Robert Stibitz
(April 30, 1904 – January 31, 1995)
Bell Labs researcher
One of the fathers of the modern first digital computer
+3
Aiken

## Slide 43
(185)10 = (0001 1000 0101)BCD (8421)
(185)10 = (10111001)2
(185)10 = (0001 1110 1011)Aiken (2421)
(185)10 = ((1+3) (8+3) (5+3))Excess-3

## Slide 44
(185)10 = (0001 1000 0101)BCD (8421)
(185)10 = (10111001)2
(185)10 = (0001 1110 1011)Aiken (2421)
(185)10 = ((4) (11) (8))Excess-3

## Slide 45
(185)10 = (0001 1000 0101)BCD (8421)
(185)10 = (10111001)2
(185)10 = (0001 1110 1011)Aiken (2421)
(185)10 = (0100 1011 1000)Excess-3

## Slide 46
Other Binary Codes
84(-2)(-1)

## Slide 47
Aiken
NOT

## Slide 48
(185)10 = (0001 1000 0101)BCD (8421)
(185)10 = (10111001)2
(185)10 = (0001 1110 1011)Aiken (2421)
(185)10 = (0100 1011 1000)Excess-3
(185)10 = (0111 1000 1011)84-2-1

## Slide 49
What’s nice about some binary codes?

## Slide 50
Self-complementing
The 9’s complement of the decimal number
=
The 1’s complement (NOT) of its binary code

## Slide 51
(185)10 = (0001 1110 1011)Aiken (2421)
(185)10 = (0100 1011 1000)Excess-3
(185)10 = (0111 1000 1011)84-2-1
9’s-comp(185)10 = (814)10
9’s-comp(185)10= NOT(0001 1110 1011)Aiken (2421)
9’s-comp(185)10= NOT(0100 1011 1000)Excess-3
9’s-comp(185)10= NOT(0111 1000 1011)84-2-1

## Slide 52
(185)10 = (0001 1110 1011)Aiken (2421)
(185)10 = (0100 1011 1000)Excess-3
(185)10 = (0111 1000 1011)84-2-1
9’s-comp(185)10 = (814)10
9’s-comp(185)10= (1110 0001 0100)Aiken (2421)
9’s-comp(185)10= (1011 0100 0111)Excess-3
9’s-comp(185)10= (1000 0111 0100)84-2-1

## Slide 53
Other Binary Codes
Gray

## Slide 55
Gray Code
Analog Digital

## Slide 56
1-bit change

## Slide 57
Gray Code
Analog Digital
Straight binary number sequence for 7 to 8: 0111 1000; causes all four bits to change values.
Gray code for 7 8: 0100 to 1100; only the first bit changes from 0 to 1; the other three bits remain the same.

## Slide 58
Gray Code
Algorithm
Step 0: Convert the decimal number to binary number.
Step 1: The MSB (Most Significant Bit) of a gray code and binary code is the same.
Step 2: The next digit of gray code is the XOR of the previous and current digit in the binary code.

## Slide 59
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code |  |  |  |  | 
Step 0: Convert the decimal number to binary number.

## Slide 60
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 |  |  |  | 
Step 1: The MSB (Most Significant Bit) of a gray code and binary code is the same.

## Slide 61
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 | 10=1 |  |  | 
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 |  |  |  | 
Step 2: The next digit of gray code is the XOR of the previous and current digit in the binary code.

## Slide 62
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 | 1 | 01=1 |  | 
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 | 1 |  |  | 
Step 2: The next digit of gray code is the XOR of the previous and current digit in the binary code.

## Slide 63
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 | 1 | 1 | 10=1 | 
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 | 1 | 1 |  | 
Step 2: The next digit of gray code is the XOR of the previous and current digit in the binary code.

## Slide 64
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 | 1 | 1 | 1 | 00=0
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 | 1 | 1 | 1 | 
Step 2: The next digit of gray code is the XOR of the previous and current digit in the binary code.

## Slide 65
(20)10 | Binary Number | 1 | 0 | 1 | 0 | 0
 | Gray Code | 1 | 1 | 1 | 1 | 0
Step 2: The next digit of gray code is the XOR of the previous and current digit in the binary code.
(21)10 | Binary Number | 1 | 0 | 1 | 0 | 1
 | Gray Code | 1 | 1 | 1 | 1 | 1

## Slide 66
ASCII Code
American Standard Code for Information Interchange

## Slide 68
“0” = (011 0000)2 = (48)10

## Slide 69
Combinational Logic
Binary Codes

## Slide 70
Combinational Logic
Code Conversion

## Slide 71
Aiken