## Slide 1
W2021: A Digital Odyssey
Notes: https://www.pinterest.ca/pin/231302130841121655/

## Slide 2
Number Systems |
Number Systems | Logic Gates |
Number Systems | Logic Gates | Combinational Logic |
Number Systems | Logic Gates | Combinational Logic | Flip-Flops |
Number Systems | Logic Gates | Combinational Logic | Flip-Flops | Sequential Logic |
Number Systems | Logic Gates | Combinational Logic | Flip-Flops| Sequential Logic | Computer Systems
(12)10 → (1100)2

## Slide 3
Minimization
aka. Simplification

## Slide 4
Minimization
Number of Gates
Number of Inputs (2-input vs 4-input)
Number of Interconnections
Propagation Time
Cost of Gates
Circuit Area
. . .
A circuit may not satisfy all due to conflicting constraints!

## Slide 5
Minimization
Boolean Algebra (algebraically)
    Needs to be smart. It is hard due to guesswork (which rules to apply?)
    If the number of variables (ABCDEF…) and/or number of minterms (MAXTERMS) grows
    No Algorithm
    Is the result minimal?!

## Slide 6
Minimization
II) Map (Karnaugh map, K-map)
aka. Graphical Manipulation

## Slide 7
Minimization
II) Map (Karnaugh map, K-map)
aka. Graphical Manipulation
Algorithm; Straightforward, up to six variables
Result is always minimal

## Slide 8
Maurice Karnaugh
Physicist
Mathematician
Inventor
Bell Labs (1954)
"The Map Method for Synthesis of
Combinational Logic Circuits”

## Slide 9
KARNAUGH MAP
/ˈkɑːrnɔː/

## Slide 10
1-Variable KARNAUGH MAP

## Slide 11
X | F
0 | m0
1 | m1
X | 
0 | 1
m0 | m1

## Slide 12
2-Variable KARNAUGH MAP

## Slide 13
Y | X | F
0 | 0 | m0
0 | 1 | m1
1 | 0 | m2
1 | 1 | m3
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3

## Slide 14
Y | X | F
0 | 0 | m0
0 | 1 | m1
1 | 0 | m2
1 | 1 | m3
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3

## Slide 15
Y | X | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
F(Y,X) = m0 = Y’X’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 0
 | 1 | 0 | 0
F(Y,X) = Y’X’ |  |  | 

## Slide 16
Y | X | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
F(Y,X) = m1 = Y’X |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 1
 | 1 | 0 | 0
F(Y,X) = Y’X |  |  | 

## Slide 17
Y | X | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m2 = YX’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 0
 | 1 | 1 | 0
F(Y,X) = YX’ |  |  | 

## Slide 18
Y | X | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
F(Y,X) = m3 = YX |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 0
 | 1 | 0 | 1
F(Y,X) = YX |  |  | 

## Slide 19
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
F(Y,X) = m0 + m1 F(Y,X) = Y’X’ + Y’X F(Y,X) = Y’(X’ + X) F(Y,X) = Y’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 0 | 0
F(Y,X) = Y’ |  |  | 

## Slide 20
Y | X | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
F(Y,X) = m2 + m3 F(Y,X) = YX’ + YX F(Y,X) = Y(X’ + X) F(Y,X) = Y |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 0
 | 1 | 1 | 1
F(Y,X) = Y |  |  | 

## Slide 21
Y | X | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
F(Y,X) = m1 + m3 F(Y,X) = Y’X + YX F(Y,X) = X(Y’ + Y) F(Y,X) = X |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 1
 | 1 | 0 | 1
F(Y,X) = X |  |  | 

## Slide 22
Y | X | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m0 + m2 F(Y,X) = Y’X’ + YX’ F(Y,X) = X’(Y’ + Y) F(Y,X) = X’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 0
 | 1 | 1 | 0
F(Y,X) = X’ |  |  | 

## Slide 23
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m0 + m1 + m2 F(Y,X) = Y’X’ + Y’X + YX’ F(Y,X) = Y’(X’ + X) + YX’ F(Y,X) = Y’ + YX’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 1 | 0
F(Y,X) = Y’ + YX’

## Slide 24
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m0 + m1 + m2 F(Y,X) = Y’X’ + Y’X + YX’ F(Y,X) = X’(Y’ + Y) + Y’X F(Y,X) = X’ + Y’X |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 1 | 0
F(Y,X) = X’ + Y’X

## Slide 25
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m0 + m1 + m2 F(Y,X) = Y’X’ + Y’X + YX’ F(Y,X) = Y’X’ + Y’X’ + Y’X + YX’ F(Y,X) = Y’(X’ + X) + Y’X’ + YX’ F(Y,X) = Y’ + Y’X’ + YX’ F(Y,X) = Y’ + X’(Y’ + Y) F(Y,X) = Y’ + X’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 1 | 0
F(Y,X) = Y’ + X’

## Slide 26
Y | X | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
F(Y,X) = m0 + m1 + m2 + m3 F(Y,X) = Y’X’ + Y’X + YX’ + YX F(Y,X) = Y’(X’ + X) + Y(X’ + X) F(Y,X) = Y’ + Y F(Y,X) = 1 |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 1
 | 1 | 1 | 1
F(Y,X) = m0+m1+m2+m3
F(Y,X) = 1

## Slide 27
Y | X | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
F(Y,X) = m1 + m2 F(Y,X) = Y’X + YX’ |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 0 | 1
 | 1 | 1 | 0
F(Y,X) = m1 + m2
F(Y,X) = Y’X + YX’

## Slide 28
Y | X | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
F(Y,X) = m0 + m3 F(Y,X) = Y’X’ + YX |  | 
 |  | X | 
 |  | 0 | 1
Y | 0 | 1 | 0
 | 1 | 0 | 1
F(Y,X) = m0 + m2
F(Y,X) = Y’X’ + YX

## Slide 29
3-Variable KARNAUGH MAP

## Slide 30
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 31
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3
 |  | X | 
 |  | 0 | 1
Y | 0 | m0 | m1
 | 1 | m2 | m3
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 32
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
Z

## Slide 33
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
Z’

## Slide 34
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
Y

## Slide 35
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
Y'

## Slide 36
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
X

## Slide 37
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
X’ ?

## Slide 38
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 39
Z | Y | X | F
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7
 |  | YX |  |  |  |  | 
 |  | 00 | 01 | 11 | 10 |  | 
Z | 0 | m0 | m1 | m3 | m2 | 0 | Z
 | 1 | m4 | m5 | m7 | m6 | 1 | 
X’
X’

## Slide 40
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?

## Slide 41
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
FX(Y,X) = Z’ +
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1

## Slide 42
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’ + ZY

## Slide 43
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’ + Y

## Slide 44
MAXTERMS

## Slide 45
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Z,Y,X) = Π M(4,5)
F(Y,X) = (Z’+Y+X) (Z’+Y+X’)
F(Y,X) = ?
F(Z,Y,X) = Π M(4,5)
F(Y,X) = ?

## Slide 46
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
F(Z,Y,X) = Π M(4,5)
F(Y,X) = (Z’+Y+X) (Z’+Y+X’)
F(Y,X) = ?
F’(Z,Y,X) = ∑ m(4,5)
F’(Y,X) = ZY’

## Slide 47
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Z,Y,X) = Π M(4,5)
F(Y,X) = (Z’+Y+X) (Z’+Y+X’)
F(Y,X) = ?
F(Z,Y,X) = Π M(4,5)
F(Y,X) = (F’)’
F(Y,X) = (ZY’)’
F(Y,X) = Z’+Y

## Slide 48
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’Y’X’+Z’Y’X+Z’YX’+Z’YX+ZYX’+ZYX
F(Y,X) = ?
F(Z,Y,X) = ∑ m(0,1,2,3,6,7)
F(Y,X) = Z’ + Y
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
F(Z,Y,X) = Π M(4,5)
F(Y,X) = (F’)’
F(Y,X) = (ZY’)’
F(Y,X) = Z’+Y
F(Z,Y,X) = Π M(4,5)
F(Y,X) = (Z’+Y+X) (Z’+Y+X’)
F(Y,X) = ?

## Slide 49
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
F(Z,Y,X) = ∑ m(0,2,4, 6)
F(Y,X) = Z’Y’X’+Z’YX’+ZY’X’+ZYX’
F(Y,X) = ?

## Slide 50
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
F(Z,Y,X) = ∑ m(0,2,4, 6)
F(Y,X) = Z’Y’X’+Z’YX’+ZY’X’+ZYX’
F(Y,X) = ?
F(Z,Y,X) = ∑ m(0,2,4, 6)
F(Y,X) = X’

## Slide 51
MAXTERMS

## Slide 52
Z | Y | X | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
F(Z,Y,X) = Π M(1,3,5,7)
F(Y,X) = (Z+Y+X’)(Z+Y’+X’)(Z’+Y+X’)(Z’+Y’+X’)
F(Y,X) = ?
F(Z,Y,X) = Π M(1,3,5,7)
F(Y,X) = (X)’
F(Y,X) = X’

## Slide 53
4-Variable KARNAUGH MAP

## Slide 54
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | m0 | m1 | m3 | m2
 | 01 | m4 | m5 | m7 | m6
 | 11 | m12 | m13 | m15 | m14
 | 10 | m8 | m9 | m11 | m10

## Slide 55
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | m0 | m1 | m3 | m2
 | 01 | m4 | m5 | m7 | m6
 | 11 | m12 | m13 | m15 | m14
 | 10 | m8 | m9 | m11 | m10

## Slide 56
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | m0 | m1 | m3 | m2
 | 01 | m4 | m5 | m7 | m6
 | 11 | m12 | m13 | m15 | m14
 | 10 | m8 | m9 | m11 | m10

## Slide 57
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | m0 | m1 | m3 | m2
 | 01 | m4 | m5 | m7 | m6
 | 11 | m12 | m13 | m15 | m14
 | 10 | m8 | m9 | m11 | m10
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)

## Slide 58
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 59
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
F (W,Z,Y,X) = Y’ +
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 60
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
F (W,Z,Y,X) = Y’ +
Warning!
W={0,1}, the value of W matters in m10
Z={0,1}
Y={1}
X={0}
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 61
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
F (W,Z,Y,X) = Y’ + W’YX’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 62
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
F (W,Z,Y,X) = Y’ + W’YX’ + WZYX’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 63
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
F (W,Z,Y,X) = Y’ + W’YX’ + ZYX’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 64
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
F (W,Z,Y,X) = Y’ + W’X’ + WYX’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 65
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∑m(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
F (W,Z,Y,X) = Y’ + W’X’ + ZX’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 66
MAXTERMS

## Slide 67
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 1
 | 10 | 1 | 1 | 0 | 0
F (W,Z,Y,X) = ∏M(3, 7, 10, 11, 15)
F (W,Z,Y,X) = (YX)’(WZ’Y)’
F (W,Z,Y,X) = (Y’+X’)(W’+Z+Y’)
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 68
Click to Play!
https://en.wikipedia.org/wiki/Karnaugh_map#/media/File:Torus_from_rectangle.gif

## Slide 69
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 0 | 0 | 1
 | 01 | 0 | 0 | 0 | 0
 | 11 | 0 | 0 | 0 | 0
 | 10 | 1 | 0 | 0 | 1
F (W,Z,Y,X) = ∑m(0, 2, 8, 10)
F (W,Z,Y,X) = Z’X’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10
torus

## Slide 70
MAXTERMS

## Slide 71
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 0 | 0 | 1
 | 01 | 0 | 0 | 0 | 0
 | 11 | 0 | 0 | 0 | 0
 | 10 | 1 | 0 | 0 | 1
F (W,Z,Y,X) = ∑m(0, 2, 8, 10)
F (W,Z,Y,X) = Z’X’
F (W,Z,Y,X) = ∏M(1,3-7,9,11-15)
F (W,Z,Y,X) = (X)’(Z)’
F (W,Z,Y,X) = X’Z’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10
torus

## Slide 72
Given two unsigned numbers x and y, design a logic circuit to see

## Slide 73
Y2 | Y1 | X2 | X1 | F(Y2,Y1,X2,X1)= m(0,1,2,3,5,6,7,10,11,15) | F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1
Y2 | Y1 | X2 | X1 |  | 
0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1

## Slide 75
 |  | X2X1 |  |  | 
 |  | 00 | 01 | 11 | 10
Y2Y1 | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚺 m(0,1,2,3,5,6,7,10,11,15)
F(Y2,Y1,X2,X1)=𝚷 M(4,8,9,12,13,14)
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 76
 |  | X2X1 |  |  | 
 |  | 00 | 01 | 11 | 10
Y2Y1 | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚺 m(0,1,2,3,5,6,7,10,11,15)
F(Y2,Y1,X2,X1)=Y’2Y’1 +
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 77
 |  | X2X1 |  |  | 
 |  | 00 | 01 | 11 | 10
Y2Y1 | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚺 m(0,1,2,3,5,6,7,10,11,15)
F(Y2,Y1,X2,X1)= Y’2Y’1 + X2X1
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 78
 |  | X2X1 |  |  | 
 |  | 00 | 01 | 11 | 10
Y2Y1 | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚺 m(0,1,2,3,5,6,7,10,11,15)
F(Y2,Y1,X2,X1)= Y’2Y’1 + X2X1 + Y’2X1
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 79
 |  | X2X1 |  |  | 
 |  | 00 | 01 | 11 | 10
Y2Y1 | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚺 m(0,1,2,3,5,6,7,10,11,15)
F(Y2,Y1,X2,X1)= Y’2Y’1 + X2X1 + Y’2X1 + Y’2X2
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 80
 |  | X2X1 |  |  | 
 |  | 00 | 01 | 11 | 10
Y2Y1 | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚺 m(0,1,2,3,5,6,7,10,11,15)
F(Y2,Y1,X2,X1)= Y’2Y’1 + X2X1 + Y’2X1 + Y’2X2 + Y’1X2
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 81
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚷 M(4,8,9,12,13,14)
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10
Change of Variable:
X1 → X
X2 → Y
Y1 → Z
Y2 → W

## Slide 82
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚷 M(4,8,9,12,13,14)
F(W,Z,Y,X)=()’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10
Change of Variable:
X1 → X
X2 → Y
Y1 → Z
Y2 → W

## Slide 83
MAXTERMS

## Slide 84
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚷 M(4,8,9,12,13,14)
F(W,Z,Y,X))=(WY’ + )’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 85
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚷 M(4,8,9,12,13,14)
F(W,Z,Y,X))=(WY’ + ZY’X’ + )’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 86
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚷 M(4,8,9,12,13,14)
F(W,Z,Y,X))=(WY’ + ZY’X’ + WZX’)’
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 87
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
WZ | 00 | 1 | 1 | 1 | 1
 | 01 | 0 | 1 | 1 | 1
 | 11 | 0 | 0 | 1 | 0
 | 10 | 0 | 0 | 1 | 1
F(Y2,Y1,X2,X1)=𝚷 M(4,8,9,12,13,14)
F(W,Z,Y,X))=(WY’ + ZY’X’ + WZX’)’
F(Y2,Y1,X2,X1)=(WY’)’ (ZY’X’)’ (WZX’)’
F(Y2,Y1,X2,X1)=(W’+Y) (Z’+Y+X)’ (W’+Z’+X)
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 88
5-Variable KARNAUGH MAP

## Slide 91
n-Variable KARNAUGH MAP

## Slide 92
n-Variable
Quine–McCluskey Algorithm
https://en.wikipedia.org/wiki/Quine%E2%80%93McCluskey_algorithm
1878 ← 1937 ← 1952 ← 1956

## Slide 93
Demo
Quine–McCluskey Algorithm
https://www.mathematik.uni-marburg.de/~thormae/lectures/ti1/code/qmc/

## Slide 94
Don’t Care Conditions
In practice, in some applications the function is not specified for certain combinations of the variables.

## Slide 95
Z | Y | X | F=if input is positive(2’s comp.) then 1 else 0
0 | 0 | 0 | ?
0 | 0 | 1 | ?
0 | 1 | 0 | ?
0 | 1 | 1 | ?
1 | 0 | 0 | ?
1 | 0 | 1 | ?
1 | 1 | 0 | ?
1 | 1 | 1 | ?

## Slide 96
Z | Y | X | F=if input is positive(2’s comp.) then 1 else 0
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
In math, 0 is not positive neither negative!

## Slide 97
Z | Y | X | F=∑m(1,2,3)=∏M(0,4,5,6,7)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 98
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 0 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
F (Z,Y,X) = ∑m(1, 2, 3)
F (W,Z,Y = Z’X + Z’Y
Boolean algebra  Z’(X+Y)

## Slide 99
MAXTERMS

## Slide 100
F(Z,Y,X) = Π M(0,4,5,6,7)
FX.(Y,X) = (Z + Y’X’)’
F(X,Y,X) = Z’ (Y+X)
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 0 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6

## Slide 101
Z | Y | X | F=if positive(2’s comp.) then 1 if negative 0
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
In math, 0 is not positive neither negative!

## Slide 102
Z | Y | X | F=if positive(2’s comp.) then 1 if negative 0
0 | 0 | 0 | ░
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 103
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | ░ | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
F (Z,Y,X) = ∑m(1, 2, 3) + ∑d(0)
F (W,Z,Y = Z’X + Z’Y

## Slide 104
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
F (Z,Y,X) = ∑m(1, 2, 3) + ∑m(0)
F (W,Z,Y = Z’
In this case, the don’t care condition help to more simplification

## Slide 105
MAXTERMS

## Slide 106
F(Z,Y,X) = Π M(4,5,6,7) + ∑D(0)
FX.(Y,X) = (Z)’
FX.(Y,X) = Z’
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | ░ | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6

## Slide 107
F(Z,Y,X) = Π M(0,4,5,6,7) + ∑M(0)
FX.(Y,X) = (Z + Y’X’)’
F(X,Y,X) = Z’ (Y+X)
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | 0 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
In this case, the don’t care condition does NOT help to more simplification

## Slide 108
Don’t Care Conditions
Functions that have unspecified outputs for some input combinations are called incompletely specified functions.
Don’t-care conditions can be used on a map to provide further simplification of the Boolean expression.

## Slide 109
Don’t Care Conditions
To distinguish the don’t-care condition from 1’s and 0’s, an X is used.
Notes: Thus, an X inside a square in the map indicates that we don’t care
whether the value of 0 or 1 is assigned to F for the particular minterm.

## Slide 110
 |  | YX |  |  | 
 |  | 00 | 01 | 11 | 10
Z | 0 | X | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
F (Z,Y,X) = ∑m(1, 2, 3) + ∑d(0)
F (Z,Y,X) = Π M(4,5,6,7) + ∑D(0)